LRU series Finger Reader SDK Development Guide

Directory

1.Fingerprint parameters

2.Fingerprint image

3.Fingerprint template

4. Constant definition

5. Function description

6. Use functions

1.Fingerprint parameters

Descriptio	specifications
FRR	0.005%
FAR	0.00008%
Interface	USB
Antistatic capacity	IEC-61000-4-2 standard >15KV
Working current	110 mA
Working temperature	-10°C ~ 60°C
Working humidity	0%~98%
Power Voltage	5V

2.Fingerprint image

The fingerprint image size is 256 x 288 or 256 x 360. 8-bit RAW image. When a function is used to obtain a fingerprint image, the declared array of received image data cannot be less than 92160. It is generally defined as 92160.
The fingerprint image has a resolution of 500DPI

3.Fingerprint template

A fingerprint template is a set of fingerprint feature points and consists of fingerprint feature points.
In the SDK, fingerprint templates are divided into reference templates and matching templates.
 The reference template is generated when the fingerprint is registered. It is generated by collecting the fingerprint image for many times.
The matching template is generated by the fingerprint image of a fingerprint collection.
Generally, the matching template is compared with the reference template to confirm the recognition result.
The reference template size is a fixed 512 bytes.
The matching template size is a fixed 256 bytes.

4. Constant definition
FPM_DEVICE=1	&&device
FPM_PLACE=02	&&Please press your finger
FPM_LIFT=03	&&Please raise your finger
FPM_CAPTURE=4	&&Image enroll is complete
FPM_GENCHAR=5	&&The collection and matching template is complete
FPM_ENRFPT=6	&&Registration is completed by reference template
FPM_NEWIMAGE=7	&&new fingerprint image
FPM_TIMEOUT =8	&&timeout
FPM_IMGVAL=9	&&Image quality
REFTPSIZE =512	&&Reference template size
MATTPSIZE =256	&&matches the template size
IMGWIDTH = 256	&&Image width
IMGHEIGHT =288	&&Image height
IMGSIZE =73728	&&Image data size
SREFTPSIZE=768	&&Reference template size (string template)
SMATTPSIZE=384	&&matches template size (string template)

5. Function description

OPEN/CLOSE Device
int WINAPI OpenDevice(int comnum,int nbaud,int style); / * Function: Open the fingerprint device / * Parameters: All three parameters are integers, used to set device parameters. 0 is used here, that is, OpenDevice(0,0,0). / * Return value: Returns an integer. If “1” is returned, the device is successfully opened; otherwise, the device fails to be opened
int WINAPI LinkDevice(); / * Function: Connect the fingerprint device and use it after the OpenDevice is successful to verify the reliability of communication / * Parameter: No parameter / * Return value: Returns an integer. If “1” is returned, the connection is successful; otherwise, the connection fails / Note: In the program, when opening the fingerprint device, both OpenDevice and LinkDevice return 1, indicating that the device is successfully opened

int WINAPI CloseDevice(); / * Function: Close the open fingerprint device / * Parameter: No parameter / * Return value: Returns an integer. If it returns” 1”, it means the shutdown was successful, otherwise the shutdown failed. Usually in a program, it is not necessary to judge the CloseDevice value

Enroll the reference template and Capture the matching template
void WINAPI EnrolFpChar(); / or / void WINAPI EnrollTemplate(); / * Function: Start to register the fingerprint reference template / * Parameter: No parameter / * Return value: There is no return value. The result is returned by the message
void WINAPI GenFpChar(); / or / void WINAPI CaptureTemplate (); / * Function: Starts to collect fingerprint matching templates / * Parameter: No parameter / * Return value: There is no return value. The result is returned by the message

Get fingerprint information
int WINAPI GetWorkMsg(); / * Function: Get fingerprint working message / * Parameter: No parameter / * Return value: Returns an integer. A number greater than “1” indicates a valid fingerprint work message. The meaning of each value is determined by the constants
int WINAPI GetRetMsg(); / * Function: Get fingerprint processing return message / * Parameter: No parameter / * Return value: Returns an integer. Returns 1, indicating that the function in the current fingerprint working mode is executed successfully; otherwise, the function fails

Obtain the corresponding data after the registration reference template and matching template are successfully collected

BOOL WINAPI GetFpCharByEnl(BYTE * fpbuf,int * fpsize); / or / BOOL WINAPI GetTemplateByEnl(BYTE * fpbuf, int * fpsize); / * Function: Obtain a reference template in binary format / * Parameters: The first parameter is the pre-allocated memory space, and the second parameter returns the actual size of the template / * Return value: Returns an integer. If 1 is returned, the acquisition succeeds; otherwise, the acquisition fails / BOOL WINAPI GetFpStrByEnl(char * fpstr); / or / BOOL WINAPI GetBase64StrByEnl(BOOL unicode, BYTE * tpstr); / * Function: Obtain a reference template in string format / * Parameters: Parameters are pre-allocated memory space / * Return value: Returns an integer. If “1” is returned, the acquisition succeeds; otherwise, the acquisition fails

BOOL WINAPI GetFpCharByGen(BYTE * tpbuf,int * tpsize); / or / BOOL WINAPI GetTemplateByCap(BYTE * fpbuf,int * fpsize); / * Function: Obtain the matching template. The obtained template is in binary format / * Parameters: The first parameter is the pre-allocated memory space, and the second parameter returns the actual size of the template / * Return value: Returns an integer. If 1 is returned, the acquisition succeeds; otherwise, the acquisition fails
BOOL WINAPI GetFpStrByGen(char * tpstr); / or / BOOL WINAPI GetBase64StrByCap(BOOL unicode,BYTE * tpstr); / * Function: Obtain a matching template. Obtain a reference template in string format / * Parameters: Parameters are pre-allocated memory space / * Return value: Returns an integer. If“ 1” is returned, the acquisition succeeds; otherwise, the acquisition fails
Note: The above functions are executed during the process of getting the fingerprint message

Comparison of templates
int WINAPI MatchTemplateOne(BYTE *pSrcData,BYTE *pDstData,int nDstSize); / * Function: Compare reference templates and matching templates in binary format / * Parameters: The first parameter is the matching template, the second parameter is the reference template, and the third parameter is the size of the reference template, which is 512 / * Return value: Indicates the score of fingerprint comparison. If the score is greater than 100, the comparison is successful. Changing the score provides a security level
int WINAPI MatchTemplateEx(char* pSrcData,char* pDstData); / * Function: Compare the reference template in string format and match the template / * Parameters: The first parameter is the matching template, the second parameter is the reference template / * Return value: Indicates the score of fingerprint comparison. If the score is greater than 100, the comparison is successful. Changing the score provides a security level
int WINAPI MatchTemplateOneEx(BYTE *pSrcData,int nSrcSize,BYTE *pDstData,int nDstSize);
* Function: Compare reference templates and reference templates in binary format / * Parameters: The first parameter is the reference template, the second parameter is the size of the reference template, the third parameter is the size of the reference template, and the fourth parameter is the size of the reference template. The two reference templates are 512 / * Return value: Indicates the score of fingerprint comparison. If the score is greater than 100, the comparison is successful. Changing the score provides a security level
Note: There are two formats for templates, and they need to correspond one to one. String format and binary format cannot be mixed together. Using templates in binary format provides speed of alignment. Using a template in string format provides ease of use.

Painting fingerprint image
int WINAPI DrawImage(HDC hdc,int left,int top); / * Function: Draw on the specified window / * Arguments: The first argument is the drawing device handle, obtained by GetDC, the second argument is the drawing X coordinate, and the third argument is the drawing Y coordinate / * Return value: integer. If 1 is returned, the drawing succeeds. If 0 is returned, the drawing fails

6. Use functions

The usage flow chart is as follows:
The template in the figure is obtained and compared in string format, as is the binary template.
In practice, the reference template is usually stored in the database with the corresponding user information at the time of registration. In the identification process, we only need to collect the matching template and compare the matching template with the reference template in the database to determine that the current finger is the finger of the user in the database. (That is, whether 1:1 or 1:N, you only need to collect the matching template once, and then use the MatchTemplateEx function to determine if the match is successful.)